Simulating Variable Density Flows in the Low-Mach Number Limit with Incompact3D

Incompact3D is a widely used flow solver providing highly scalable, high (6th) order accurate capabilities for simulating incompressible turbulent flows, an efficient spectral Poisson solver providing the divergence-free condition up to machine accuracy. The QuasIncompact3D solver presented in this talk is a newly developed solver for the Low Mach Number (LMN) approximation of low speed variable density flows.
In implementing the LMN approximation equations, two approaches for the Poisson equation are possible: one yielding a constant-coefficient Poisson equation, similar to the incompressible case; and one yielding a variable-coefficient Poisson equation. The variable-coefficient Poisson equation has theoretical advantages, guaranteeing the satisfaction of the LMN approximation equations, however spectral Poisson solvers can only solve constant-coefficient Poisson equations, hence an iterative approach is required. In this work, both constant-coefficient and variable-coefficient Poisson solvers are implemented and a new density interpolation is proposed to improve convergence rates, potentially saving significant computational effort.
Results for strong and weak scaling tests on both EPCC’s ARCHER, and CINECA’s Marconi machines will be presented alongside investigations of variable-density, low-speed flows: a non-isothermal mixing layer, a turbulent buoyant jet and a non-Boussinesq gravity current.

Key words:

Low Mach Number flows
Poisson Solvers
High Performance Computing